## Slide 1: A Hands-On Introduction to Computational Fluid Dynamics
Mohammad Umair†, Gerardo Zampino† and Ricardo Vinuesa†
†FLOW, Engineering Mechanics, KTH Royal Institute of Technology, Sweden

## Slide 2: Computational Fluid Dynamics
PURE
EXPERIMENTS
17th Century
France and England

## Slide 3: Computational Fluid Dynamics
PURE
EXPERIMENTS
PURE
THEORY
17th Century
18th – 19th Century
France and England
Europe

## Slide 4: Computational Fluid Dynamics
PURE
EXPERIMENTS
PURE
THEORY
17th Century
18th – 19th Century
France and England
Europe
20th Century

## Slide 5: Computational Fluid Dynamics
A new “third approach” in the philosophical study of fluid dynamics
PURE
EXPERIMENTS
PURE
THEORY
CFD
17th Century
18th – 19th Century
France and England
Europe
20th Century

## Slide 6: Computational Fluid Dynamics
PURE
EXPERIMENTS
PURE
THEORY
CFD
17th Century
18th – 19th Century
France and England
Europe
20th Century
A new “third approach” in the philosophical study of fluid dynamics
(Nothing more than that!)

## Slide 7: Computational Fluid Dynamics
A new “third approach” in the philosophical study of fluid dynamics
(Nothing more than that!)
PURE
EXPERIMENTS
PURE
THEORY
CFD
17th Century
18th – 19th Century
France and England
Europe
20th Century
Just to keep things in perspective:
CFD nicely compliments the other two approaches but will never replace either of them - as sometimes suggested!

## Slide 8: Computational Fluid Dynamics
A new “third approach” in the philosophical study of fluid dynamics
(Nothing more than that!)
PURE
EXPERIMENTS
PURE
THEORY
CFD
17th Century
18th – 19th Century
France and England
Europe
20th Century
Just to keep things in perspective:
CFD nicely compliments the other two approaches but will never replace either of them - as sometimes suggested!
Future advancement will rest upon a proper balance of all three approaches, with CFD helping to interpret results of theories and experiments, and vice-versa.

## Slide 9: CFD as a research tool
CFD results are directly analogous to Wind Tunnel results.
However, unlike a wind tunnel a computer program can be carried everywhere or can be accessed sitting 1000 miles away!
A CFD program is, therefore, a “readily transportable wind tunnel”, where you can carry out “numerical experiments”.

## Slide 10: CFD as a research tool: Who cares?

## Slide 11: CFD as a research tool: Who cares?
Aviation

## Slide 12: CFD as a research tool: Who cares?
Automotive
Aviation

## Slide 13: CFD as a research tool: Who cares?
Turbomachines
Automotive
Aviation

## Slide 14: CFD as a research tool: Who cares?
HVAC
Turbomachines
Automotive
Aviation

## Slide 15: CFD as a research tool: Who cares?
Cities
HVAC
Turbomachines
Automotive
Aviation

## Slide 16: CFD as a research tool: Who cares?
Cities
HVAC
Turbomachines
Automotive
Aviation
+ many more !

## Slide 17: So How to CFD?
CFD involves:
Identifying the physical phenomenon, that includes Governing equations, Initial & Boundary conditions.
Breaking down the continuous problem to a discrete representation.
Solving the discrete set of equations using adequate numerical methods.
Post processing the results.

## Slide 18: What are we solving?
Navier Stokes equations
Continuity equation:
Momentum equation:
Energy equation:
Depending on the nature of physics governing the fluid motion one or more terms might be negligible.
Presence of each term and their combinations determines the appropriate solution algorithm and the numerical procedure.

## Slide 19: Classification of PDEs
Elliptic
Parabolic
Hyperbolic
Equations belonging to each of these classifications behave in different ways both physically and numerically.
Potential Flow
Flow over an oscillating plate
(Stokes 2nd Problem)
Wave motion

## Slide 20: Techniques for Numerical Discretization
Commonly used discretization methods
Governing Equations
Numerical Analogue
Discretization
Finite Difference Methods
Finite Volume Methods
Spectral
Methods
Finite/Spectral Element Methods

## Slide 21: Techniques for Numerical Discretization
Commonly used discretization methods
Governing Equations
Numerical Analogue
Discretization
Finite Difference Methods
Finite Volume Methods
Spectral
Methods
Finite/Spectral Element Methods
TODAY
TOMORROW

## Slide 22: Finite Difference Method
Definition of a derivative
Exact

## Slide 23: Finite Difference Method
Definition of a derivative
Exact

## Slide 24: Finite Difference Method
Definition of a derivative
Exact

## Slide 25: Finite Difference Method
Finite Difference

## Slide 26: Finite Difference Method
Finite Difference

## Slide 27: Finite Difference Method
Finite Difference
Forward

## Slide 28: Finite Difference Method
Finite Difference
Forward
Backward

## Slide 29: Finite Difference Method
Finite Difference
Forward
Backward
Centered

## Slide 30: Finite Difference Method
Finite Difference
Forward
Backward
Centered
How good is the approximation?

## Slide 31
How good is the approximation?

## Slide 32
How good is the approximation?
Taylor Series

## Slide 33
How good is the approximation?
Taylor Series

## Slide 34
How good is the approximation?
Taylor Series

## Slide 35
How good is the approximation?
Taylor Series

## Slide 36
How good is the approximation?
Taylor Series
1st order accurate

## Slide 37
Second derivative

## Slide 38
Second derivative

## Slide 39
Second derivative

## Slide 40
Second derivative
Central Differencing formula for 2nd derivative

## Slide 41: Derivative Operators
Taylor Series

## Slide 42: Derivative Operators
Taylor Series

## Slide 43: Derivative Operators
Taylor Series

## Slide 44: Derivative Operators

## Slide 45: Derivative Operators
Inversion
1st Derivative

## Slide 46: Derivative Operators
Inversion
1st Derivative

## Slide 47: Derivative Operators
Inversion
1st Derivative

## Slide 48: Derivative Operators
Inversion
1st Derivative
Inversion
2nd Derivative

## Slide 49: Finite Difference in action
1D Linear Convection

## Slide 50: Finite Difference in action
1D Linear Convection
Initial Condition:
Exact Solution:

## Slide 51: Finite Difference in action
1D Linear Convection
With an Initial Condition (given as a wave), the equation represents propagation of a wave with a speed c, without change in its shape!
Initial Condition:
Exact Solution:

## Slide 52: Finite Difference in action
1D Linear Convection
With an Initial Condition (given as a wave), the equation represents propagation of a wave with a speed c, without change in its shape!
Initial Condition:
Exact Solution:

## Slide 53: Finite Difference in action
1D Linear Convection

## Slide 54: Finite Difference in action
1D Linear Convection
Backward Difference

## Slide 55: Finite Difference in action
1D Linear Convection
Backward Difference
Forward Euler

## Slide 56: Finite Difference in action
1D Linear Convection
Backward Difference
Forward Euler

## Slide 57: Finite Difference in action
1D Linear Convection
Backward Difference
Forward Euler

## Slide 58: Finite Difference in action
1D Linear Convection
Backward Difference
Forward Euler
Let’s write our 1st CFD code !
Barba et al., (2018). CFD Python: the 12 steps to Navier-Stokes equations. Journal of Open-Source Education, 1(9), 21. https://doi.org/10. 21105/jose.00021

## Slide 59
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys

## Slide 60
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1

## Slide 61
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function

## Slide 62
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)

## Slide 63
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 64
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 65
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?

## Slide 66
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?
Let’s try with central differencing !

## Slide 67
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?
Let’s try with central differencing !
Change these !

## Slide 68
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx-1):
u[i] = un[i] – c * dt/dx * (un[i+1]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?
Let’s try with central differencing !
Change these !

## Slide 69
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx-1):
u[i] = un[i] – c * dt/dx * (un[i+1]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?
Let’s try with central differencing !

## Slide 70
1st Code: 1D Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx-1):
u[i] = un[i] – c * dt/dx * (un[i+1]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Ok, so our hat function moved to the right, but it’s no longer a hat. What’s going on?
Let’s try with central differencing !
What’s that !

## Slide 71
1D Linear Convection with Central Differencing in Space

## Slide 72
1D Linear Convection with Central Differencing in Space

## Slide 73
1D Linear Convection with Central Differencing in Space

## Slide 74
1D Linear Convection with Central Differencing in Space

## Slide 75
1D Linear Convection with Central Differencing in Space

## Slide 76
1D Linear Convection with Central Differencing in Space
Truncation Error

## Slide 77
1D Linear Convection with Central Differencing in Space
Truncation Error
As Numerical Scheme is Consistent

## Slide 78
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 79
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 80
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 81
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 82
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 83
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 84
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 85
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation !

## Slide 86
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation !
NOT a convection equation, It is a Convection-Diffusion equation !!

## Slide 87
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation !
NOT a convection equation, It is a Convection-Diffusion equation !!
-ve Diffusion Coefficient !!

## Slide 88
1D Linear Convection with Central Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation !
NOT a convection equation, It is a Convection-Diffusion equation !!
-ve Diffusion Coefficient !!
Explosion : Unstable Scheme !!

## Slide 89
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:

## Slide 90
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!

## Slide 91
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!
Diffusion Coefficient must be +ve !!

## Slide 92
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!
Diffusion Coefficient must be +ve !!
For stability, we need:

## Slide 93
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!
Diffusion Coefficient must be +ve !!
For stability, we need:
Courant-Friedrich-Lewy (CFL) Number!!

## Slide 94
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!
Diffusion Coefficient must be +ve !!
For stability, we need:
Courant-Friedrich-Lewy (CFL) Number!!
For a CFL of Numerical Diffusion is of

## Slide 95
1D Linear Convection with Backward Differencing in Space
Consider the exact solution of the discretized equation:
Modified Differential Equation:
Convection-Diffusion equation !!
Diffusion Coefficient must be +ve !!
For stability, we need:
Courant-Friedrich-Lewy (CFL) Number!!
Poor Accuracy !!
For a CFL of Numerical Diffusion is of

## Slide 96
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 97
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – c * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Change this only !

## Slide 98
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – un[i] * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 99
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – un[i] * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 100
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
dt = 0.025
c = 1
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – un[i] * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Let’s introduce CFL

## Slide 101
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
CFL = 0.9
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – un[i] * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Let’s introduce CFL
dt = CFL*dx/max(abs(u))

## Slide 102
2nd Code: 1D non-Linear Convection
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41
dx = 2/(nx-1)
nt = 25
CFL = 0.9
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx):
u[i] = un[i] – un[i] * dt/dx * (un[i]-un[i-1])
plt.plot(np.linspace(0,2,nx), u)
Let’s introduce CFL
dt = CFL*dx/max(abs(u))
Play a bit & see what happens!

## Slide 103
3rd Code: 1D Diffusion

## Slide 104
3rd Code: 1D Diffusion
Exact Solution is known for constant

## Slide 105
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:

## Slide 106
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:

## Slide 107
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:
Leading to the solution:

## Slide 108
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:
Leading to the solution:
Exponential Damping for

## Slide 109
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:
Leading to the solution:
Exponential Damping for
Diffusion is isotropic in nature

## Slide 110
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:
Leading to the solution:
Exponential Damping for
Diffusion is isotropic in nature
No Directional Bias

## Slide 111
3rd Code: 1D Diffusion
Exact Solution is known for constant
Consider solution of type:
Introducing in the PDE, we obtain:
Leading to the solution:
Exponential Damping for
Diffusion is isotropic in nature
No Directional Bias
Central-Differencing

## Slide 112
Central Difference
Forward Euler
3rd Code: 1D Diffusion

## Slide 113
Central Difference
Forward Euler
3rd Code: 1D Diffusion

## Slide 114
Central Difference
Forward Euler
Let’s Code It !
3rd Code: 1D Diffusion

## Slide 115
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41; dx = 2/(nx-1)
nt = 25
nu = 0.3
sigma = 0.2
dt = sigma * dx**2 / nu
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
3rd Code: 1D Diffusion

## Slide 116
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41; dx = 2/(nx-1)
nt = 25
nu = 0.3
sigma = 0.2
dt = sigma * dx**2 / nu
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
3rd Code: 1D Diffusion
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx-1):
u[i] = un[i] + nu * dt/dx**2 * (un[i+1]-2*un[i]+un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 117
import numpy as np
import matplotlib.pyplot as plt
import time, sys
nx = 41; dx = 2/(nx-1)
nt = 25
nu = 0.3
sigma = 0.2
dt = sigma * dx**2 / nu
The initial velocity is given as in the interval and elsewhere in Hat function
u = np.ones(nx)
u[int(0.5/dx):int(1/dx+1)] = 2
print(u)
plt.plot(np.linspace(0,2,nx), u)
3rd Code: 1D Diffusion
un = np.ones(nx)
for n in range(nt):
un=u.copy()
for i in range(1,nx-1):
u[i] = un[i] + nu * dt/dx**2 * (un[i+1]-2*un[i]+un[i-1])
plt.plot(np.linspace(0,2,nx), u)

## Slide 118
1D Diffusion (Caution!)

## Slide 119
1D Diffusion (Caution!)
Parabolic PDE

## Slide 120
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution

## Slide 121
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:

## Slide 122
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 123
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:
Our numerical scheme does not receive information from current time !
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 124
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:
Our numerical scheme does not receive information from current time !
“Explicit Formulation”
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 125
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:
Our numerical scheme does not receive information from current time !
“Explicit Formulation”
Boundary Conditions
are lagging!
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 126
1D Diffusion (Caution!)
Parabolic PDE
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our Numerical Formulation:
Our numerical scheme does not receive information from current time !
“Explicit Formulation”
Boundary Conditions
are lagging!
Problem if Boundary Conditions are time-dependent!
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 127
1D Diffusion (Caution!)
Parabolic PDE
Our Numerical Formulation:
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our numerical scheme does not receive information from current time !
Boundary Conditions
are lagging!
“Explicit Formulation”
Problem if Boundary Conditions are time-dependent!
How can we include BCs
at current time?
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 128
1D Diffusion (Caution!)
Parabolic PDE
Our Numerical Formulation:
Characteristic lines are lines of constant ‘t’
All information at a given time should affect the solution
Our numerical scheme does not receive information from current time !
Boundary Conditions
are lagging!
“Explicit Formulation”
Problem if Boundary Conditions are time-dependent!
How can we include BCs
at current time?
“Implicit Formulation”
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 129
1D Diffusion (Implicit Formulation)
Parabolic PDE

## Slide 130
1D Diffusion (Implicit Formulation)
Parabolic PDE

## Slide 131
1D Diffusion (Implicit Formulation)
Parabolic PDE
Rearrange:

## Slide 132
1D Diffusion (Implicit Formulation)
Parabolic PDE
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
Rearrange:

## Slide 133
1D Diffusion (Implicit Formulation)
Parabolic PDE
“Implicit Formulation”
Rearrange:
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 134
1D Diffusion (Implicit Formulation)
Parabolic PDE
“Implicit Formulation”
Need Algorithms to solve such a sparse matrix system!
Rearrange:
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 135
1D Diffusion (Implicit Formulation)
Parabolic PDE
“Implicit Formulation”
Need Algorithms to solve such a sparse matrix system!
Direct or Iterative
Methods
Rearrange:
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 136
1D Diffusion (Implicit Formulation)
Parabolic PDE
“Implicit Formulation”
Need Algorithms to solve such a sparse matrix system!
Direct or Iterative
Methods
Can be Expensive!
Rearrange:
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil

## Slide 137
Crank-Nicholson Method
Well-known for Parabolic PDEs
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1

## Slide 138
Crank-Nicholson Method
Well-known for Parabolic PDEs
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1

## Slide 139
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1

## Slide 140
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1

## Slide 141
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1
n+1/2

## Slide 142
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1
n+1/2
Explicit:

## Slide 143
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1
n+1/2
Explicit:
Implicit:

## Slide 144
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1
n+1/2
Explicit:
Implicit:
2nd order in time & space !

## Slide 145
Crank-Nicholson Method
Well-known for Parabolic PDEs
n+1
n
i-1
i
i+1
i-1
i
i+1
time
Space
Stencil
[“Implicit Formulation”
+
“Explicit Formulation”]
2
1
n+1/2
Explicit:
Implicit:
2nd order in time & space !
Tridiagonal system to solve!

## Slide 146
4th Code: 1D Burger’s Equation

## Slide 147
4th Code: 1D Burger’s Equation

## Slide 148
4th Code: 1D Burger’s Equation

## Slide 149
4th Code: 1D Burger’s Equation
Initial Condition:
Exact Solution:
Boundary Condition:
Periodic BC!

## Slide 150
Let’s Code It!
4th Code: 1D Burger’s Equation
Initial Condition:
Exact Solution:
Boundary Condition:
Periodic BC!

## Slide 151
import numpy as np
import sympy as sp
import pylab as pl
pl.ion()
4th Code: 1D Burger’s Equation

## Slide 152
import numpy as np
import sympy as sp
import pylab as pl
pl.ion()
4th Code: 1D Burger’s Equation
x, nu, t = sp.symbols('x nu t')
phi = sp.exp(-(x-4*t)**2/(4*nu*(t+1))) + sp.exp(-(x-4*t-2*sp.pi)**2/(4*nu*(t+1)))
phiprime = phi.diff(x)
u = -2*nu*(phiprime/phi)+4
from sympy.utilities.lambdify import lambdify
ufunc = lambdify ((t, x, nu), u)

## Slide 153
import numpy as np
import sympy as sp
import pylab as pl
pl.ion()
nx = 101
dx = 2*np.pi/(nx-1)
nt = 100
nu = 0.07
dt = dx*nu
T = nt*dt
grid = np.linspace(0, 2*np.pi, nx)
u = np.empty(nx)
t = 0
u = np.asarray([ufunc(t, x, nu) for x in grid])
pl.figure(figsize=(11,7), dpi=100)
pl.plot(grid,u, marker='o', lw=2)
pl.xlim([0,2*np.pi])
pl.ylim([0,10])
pl.xlabel('X')
pl.ylabel('Velocity')
pl.title('1D Burgers Equation - Initial condition')
4th Code: 1D Burger’s Equation
x, nu, t = sp.symbols('x nu t')
phi = sp.exp(-(x-4*t)**2/(4*nu*(t+1))) + sp.exp(-(x-4*t-2*sp.pi)**2/(4*nu*(t+1)))
phiprime = phi.diff(x)
u = -2*nu*(phiprime/phi)+4
from sympy.utilities.lambdify import lambdify
ufunc = lambdify ((t, x, nu), u)

## Slide 154
import numpy as np
import sympy as sp
import pylab as pl
pl.ion()
nx = 101
dx = 2*np.pi/(nx-1)
nt = 100
nu = 0.07
dt = dx*nu
T = nt*dt
grid = np.linspace(0, 2*np.pi, nx)
u = np.empty(nx)
t = 0
u = np.asarray([ufunc(t, x, nu) for x in grid])
pl.figure(figsize=(11,7), dpi=100)
pl.plot(grid,u, marker='o', lw=2)
pl.xlim([0,2*np.pi])
pl.ylim([0,10])
pl.xlabel('X')
pl.ylabel('Velocity')
pl.title('1D Burgers Equation - Initial condition')
4th Code: 1D Burger’s Equation
x, nu, t = sp.symbols('x nu t')
phi = sp.exp(-(x-4*t)**2/(4*nu*(t+1))) + sp.exp(-(x-4*t-2*sp.pi)**2/(4*nu*(t+1)))
phiprime = phi.diff(x)
u = -2*nu*(phiprime/phi)+4
from sympy.utilities.lambdify import lambdify
ufunc = lambdify ((t, x, nu), u)
for n in range(nt):
un = u.copy()
for i in range(nx-1):
u[i] = un[i] - un[i] * dt/dx * (un[i]-un[i-1]) + \
nu * dt/(dx**2) * (un[i+1] - 2*un[i] + un[i-1])
# infer the periodicity
u[-1] = un[-1] - un[-1] * dt/dx * (un[-1]-un[-2]) + \
nu * dt/(dx**2) * (un[0] - 2*un[-1] + un[-2])
u_analytical = np.asarray([ufunc(T, xi, nu) for xi in grid])
pl.figure(figsize=(11,7), dpi=100)
pl.plot(grid, u, marker='o', lw=2, label='Computational')
pl.plot(grid, u_analytical, label='Analytical')
pl.xlim([0, 2*np.pi])
pl.ylim([0,10])
pl.legend()
pl.xlabel('X')
pl.ylabel('Velocity')
pl.title('1D Burgers Equation - Solutions')

## Slide 155
import numpy as np
import sympy as sp
import pylab as pl
pl.ion()
nx = 101
dx = 2*np.pi/(nx-1)
nt = 100
nu = 0.07
dt = dx*nu
T = nt*dt
grid = np.linspace(0, 2*np.pi, nx)
u = np.empty(nx)
t = 0
u = np.asarray([ufunc(t, x, nu) for x in grid])
pl.figure(figsize=(11,7), dpi=100)
pl.plot(grid,u, marker='o', lw=2)
pl.xlim([0,2*np.pi])
pl.ylim([0,10])
pl.xlabel('X')
pl.ylabel('Velocity')
pl.title('1D Burgers Equation - Initial condition')
4th Code: 1D Burger’s Equation
x, nu, t = sp.symbols('x nu t')
phi = sp.exp(-(x-4*t)**2/(4*nu*(t+1))) + sp.exp(-(x-4*t-2*sp.pi)**2/(4*nu*(t+1)))
phiprime = phi.diff(x)
u = -2*nu*(phiprime/phi)+4
from sympy.utilities.lambdify import lambdify
ufunc = lambdify ((t, x, nu), u)
for n in range(nt):
un = u.copy()
for i in range(nx-1):
u[i] = un[i] - un[i] * dt/dx * (un[i]-un[i-1]) + \
nu * dt/(dx**2) * (un[i+1] - 2*un[i] + un[i-1])
# infer the periodicity
u[-1] = un[-1] - un[-1] * dt/dx * (un[-1]-un[-2]) + \
nu * dt/(dx**2) * (un[0] - 2*un[-1] + un[-2])
u_analytical = np.asarray([ufunc(T, xi, nu) for xi in grid])
pl.figure(figsize=(11,7), dpi=100)
pl.plot(grid, u, marker='o', lw=2, label='Computational')
pl.plot(grid, u_analytical, label='Analytical')
pl.xlim([0, 2*np.pi])
pl.ylim([0,10])
pl.legend()
pl.xlabel('X')
pl.ylabel('Velocity')
pl.title('1D Burgers Equation - Solutions')

## Slide 156
5th Code: 2D Laplace Equation

## Slide 157
5th Code: 2D Laplace Equation

## Slide 158
5th Code: 2D Laplace Equation

## Slide 159
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil

## Slide 160
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
No time dependence !
5 points stencil

## Slide 161
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
No time dependence !
Calculates an equilibrium state given the specified BCs
5 points stencil

## Slide 162
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
No time dependence !
Calculates an equilibrium state given the specified BCs
Need to solve iteratively
Will reach equilibrium as iterations
Need to specify a threshold!
5 points stencil

## Slide 163
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
No time dependence !
Calculates an equilibrium state given the specified BCs
Need to solve iteratively
Will reach equilibrium as iterations
Need to specify a threshold!
5 points stencil
Let’s Code It!
BCs:

## Slide 164
5th Code: 2D Laplace Equation
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
No time dependence !
Calculates an equilibrium state given the specified BCs
Need to solve iteratively
Will reach equilibrium as iterations
Need to specify a threshold!
5 points stencil
BCs:

## Slide 165
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation

## Slide 166
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)

## Slide 167
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def laplace2D(p,y,dx,dy,target_norm):
norm=1
pn = np.empty_like(p)
while norm > target_norm:
pn = p.copy()
p[1:-1,1:-1] = (
(dy**2 * (pn[1:-1,2:] – pn[1:-1,:-2])) +
(dx**2 * (pn[2:,1:-1] – pn[:-2,1:-1]))
) / (2* (dx**2 + dy**2))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn)))
return p

## Slide 168
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def laplace2D(p,y,dx,dy,target_norm):
norm=1
pn = np.empty_like(p)
while norm > target_norm:
pn = p.copy()
p[1:-1,1:-1] = (
(dy**2 * (pn[1:-1,2:] – pn[1:-1,:-2])) +
(dx**2 * (pn[2:,1:-1] – pn[:-2,1:-1]))
) / (2* (dx**2 + dy**2))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn)))
return p
nx = 31; ny = 31; dx = 2/(nx-1); dy =1/(ny-1)
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 169
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def laplace2D(p,y,dx,dy,target_norm):
norm=1
pn = np.empty_like(p)
while norm > target_norm:
pn = p.copy()
p[1:-1,1:-1] = (
(dy**2 * (pn[1:-1,2:] – pn[1:-1,:-2])) +
(dx**2 * (pn[2:,1:-1] – pn[:-2,1:-1]))
) / (2* (dx**2 + dy**2))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn)))
return p
p = np.zeros((ny,nx))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
plot2D(x,y,p)
nx = 31; ny = 31; dx = 2/(nx-1); dy =1/(ny-1)
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 170
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
5th Code: 2D Laplace Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def laplace2D(p,y,dx,dy,target_norm):
norm=1
pn = np.empty_like(p)
while norm > target_norm:
pn = p.copy()
p[1:-1,1:-1] = (
(dy**2 * (pn[1:-1,2:] + pn[1:-1,:-2])) +
(dx**2 * (pn[2:,1:-1] + pn[:-2,1:-1]))
) / (2* (dx**2 + dy**2))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn)))
return p
p = np.zeros((ny,nx))
p[:,0] = 0 # p=0 at x=0
p[:,-1]= y # p=y at x=2
p[0,:] = p[1,:] # dp/dy=0 at y=0
p[-1,:] = p[-2,:] # dp/dy=0 at y=1
plot2D(x,y,p)
p = laplace2D(p,y,dx,dy,1e-4)
plot2D(x,y,p)
nx = 31; ny = 31; dx = 2/(nx-1); dy =1/(ny-1)
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 171
Navier-Stokes equations for incompressible flows
Continuity equation:
Momentum equation:

## Slide 172
Navier-Stokes equations for incompressible flows
Continuity equation:
Momentum equation:
No equation for pressure !

## Slide 173
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !

## Slide 174
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !

## Slide 175
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!

## Slide 176
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.

## Slide 177
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.

## Slide 178
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.

## Slide 179
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.
0
0

## Slide 180
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.
0
0

## Slide 181
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.
0
0
Pressure Poisson
Equation

## Slide 182
Navier-Stokes equations for incompressible flows
There is no obvious way of coupling these equations !
Continuity equation:
Momentum equation:
No equation for pressure !
Provides a kinematic constraint that requires pressure field to evolve such that the velocity field remains solenoidal !
Remedy: “Construct” a pressure field that guarantees continuity constraint!
Such a relation can be obtained by taking the divergence of the momentum equation.
0
0
Pressure Poisson
Equation
Let’s look at the 6th code to learn how to solve a Poisson’s equation.

## Slide 183
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation

## Slide 184
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field

## Slide 185
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:

## Slide 186
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil

## Slide 187
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil
Source term:
2 Spikes

## Slide 188
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil
Source term:
2 Spikes
The iteration will relax the initial spikes!

## Slide 189
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil
BCs:
Source term:
2 Spikes
The iteration will relax the initial spikes!

## Slide 190
6th Code: 2D Poisson’s Equation
Obtained by adding a source term on the right-hand side of the Laplace’s equation
Poisson’s equation act to “relax” the initial sources in the field
Discretized form:
i-1,j-1
i,j-1
i+1,j-1
i-1,j
i,j
i+1,j+1
y
X
i-1,j+1
i,j+1
i+1,j+1
5 points stencil
BCs:
Source term:
2 Spikes
The iteration will relax the initial spikes!
Let’s Code it!

## Slide 191
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation

## Slide 192
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)

## Slide 193
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def poisson2D(p,b,dx,dy,target_norm):
norm=1; small=1e-8; niter=0
pn = np.zeros_like(p)
while norm > target_norm:
pn = p.copy(); niter+=1
p[1:-1,1:-1] = ( ( dy**2 * (pn[2:,1:-1] – pn[:-2,1:-1]) +
dx**2 * (pn[1:-1,2:] – pn[1:-1,:-2]) -
dx**2 * dy**2 * b[1:-1,1:-1] ) /
(2* (dx**2 + dy**2)))
p[0,:] = 0 # p=0 at x=0
p[-1,:] = 0 # p=0 at x=2
p[:,0] = 0 # p=0 at y=0
p[:,-1] = 0 # p=0 at y=2
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn))+small)
return p

## Slide 194
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,2)
ax.view_init(30,225)
def poisson2D(p,b,dx,dy,target_norm):
norm=1; small=1e-8; niter=0
pn = np.zeros_like(p)
while norm > target_norm:
pn = p.copy(); niter+=1
p[1:-1,1:-1] = ( ( dy**2 * (pn[2:,1:-1] – pn[:-2,1:-1]) +
dx**2 * (pn[1:-1,2:] – pn[1:-1,:-2]) -
dx**2 * dy**2 * b[1:-1,1:-1] ) /
(2* (dx**2 + dy**2)))
p[0,:] = 0 # p=0 at x=0
p[-1,:] = 0 # p=0 at x=2
p[:,0] = 0 # p=0 at y=0
p[:,-1] = 0 # p=0 at y=2
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn))+small)
return p
nx = 51; ny = 51; dx = 2/(nx-1); dy = 2/(ny-1); nt = 100;
x = np.linspace(0, 2, nx); y = np.linspace(0, 2, ny)

## Slide 195
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def poisson2D(p,b,dx,dy,target_norm):
norm=1; small=1e-8; niter=0
pn = np.zeros_like(p)
while norm > target_norm:
pn = p.copy(); niter+=1
p[1:-1,1:-1] = ( ( dy**2 * (pn[2:,1:-1] – pn[:-2,1:-1]) +
dx**2 * (pn[1:-1,2:] – pn[1:-1,:-2]) -
dx**2 * dy**2 * b[1:-1,1:-1] ) /
(2* (dx**2 + dy**2)))
p[0,:] = 0 # p=0 at x=0
p[-1,:] = 0 # p=0 at x=2
p[:,0] = 0 # p=0 at y=0
p[:,-1] = 0 # p=0 at y=2
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn))+small)
return p
p = np.zeros((nx,ny))
b = np.zeros((nx,ny))
b[int(nx/4), int(3*ny/4)] = -100
b[int(3*nx/4), int(ny/4)] = 100
plot2D(x,y,p)
plot2D(x,y,b)
nx = 51; ny = 51; dx = 2/(nx-1); dy = 2/(ny-1); nt = 100;
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 196
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def poisson2D(p,b,dx,dy,target_norm):
norm=1; small=1e-8; niter=0
pn = np.zeros_like(p)
while norm > target_norm:
pn = p.copy(); niter+=1
p[1:-1,1:-1] = ( ( dy**2 * (pn[2:,1:-1] – pn[:-2,1:-1]) +
dx**2 * (pn[1:-1,2:] – pn[1:-1,:-2]) -
dx**2 * dy**2 * b[1:-1,1:-1] ) /
(2* (dx**2 + dy**2)))
p[0,:] = 0 # p=0 at x=0
p[-1,:] = 0 # p=0 at x=2
p[:,0] = 0 # p=0 at y=0
p[:,-1] = 0 # p=0 at y=2
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn))+small)
return p
p = np.zeros((nx,ny))
b = np.zeros((nx,ny))
b[int(nx/4), int(3*ny/4)] = -100
b[int(3*nx/4), int(ny/4)] = 100
plot2D(x,y,p)
plot2D(x,y,b)
p, niter = poisson2D(p,b,dx,dy,1e-4)
nx = 51; ny = 51; dx = 2/(nx-1); dy = 2/(ny-1); nt = 100;
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 197
import numpy as np
from matplotlib import pyplot, cm
from mpl_toolkits.mplot3d import Axes3D
6th Code: 2D Poisson’s Equation
def plot2D(x,y,p):
fig = pyplot.figure( figsize=(11,7), dpi=100 )
ax = fig.gca(projection=‘3d’)
X, Y = np.meshgrid(x,y)
surf = ax.plot_surface( X, Y, p[:], rstride=1, cstride=1, cmap=cm.viridis,
linewidth=0, antialiased=False )
ax.set_xlabel(“$x$”); ax.set_xlim(0,2)
ax.set_ylabel(“$y$”); ax.set_ylim(0,1)
ax.view_init(30,225)
def poisson2D(p,b,dx,dy,target_norm):
norm=1; small=1e-8; niter=0
pn = np.zeros_like(p)
while norm > target_norm:
pn = p.copy(); niter+=1
p[1:-1,1:-1] = ( ( dy**2 * (pn[2:,1:-1] – pn[:-2,1:-1]) +
dx**2 * (pn[1:-1,2:] – pn[1:-1,:-2]) -
dx**2 * dy**2 * b[1:-1,1:-1] ) /
(2* (dx**2 + dy**2)))
p[0,:] = 0 # p=0 at x=0
p[-1,:] = 0 # p=0 at x=2
p[:,0] = 0 # p=0 at y=0
p[:,-1] = 0 # p=0 at y=2
norm = (np.sum(np.abs(p)) – np.sum(np.abs(pn)))/(np.sum(np.abs(pn))+small)
return p, niter
p = np.zeros((nx,ny))
b = np.zeros((nx,ny))
b[int(nx/4), int(3*ny/4)] = -100
b[int(3*nx/4), int(ny/4)] = 100
plot2D(x,y,p)
plot2D(x,y,b)
p, niter = poisson2D(p,b,dx,dy,1e-4)
plot2D(x,y,p)
nx = 51; ny = 51; dx = 2/(nx-1); dy = 2/(ny-1); nt = 100;
x = np.linspace(0, 2, nx); y = np.linspace(0, 1, ny)

## Slide 198
Practical Session: 2D Lid Driven Cavity Flow

## Slide 199
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:

## Slide 200
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:

## Slide 201
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:

## Slide 202
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:
What about the pressure?

## Slide 203
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:
What about the pressure?
Recall: The pressure Poisson’s Equation

## Slide 204
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:
What about the pressure?
Recall: The pressure Poisson’s Equation

## Slide 205
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:
What about the pressure?
Recall: The pressure Poisson’s Equation
Now it’s your turn to discretize the equations, code it & visualize the results!

## Slide 206
Practical Session: 2D Lid Driven Cavity Flow
Continuity:
Momentum:
X-velocity:
Y-velocity:
What about the pressure?
Recall: The pressure Poisson’s Equation
Now it’s your turn to discretize the equations, code it & visualize the results!
Good Luck!

## Slide 207: References
CFD Python: 12 steps to Navier-Stokes :: Lorena A. Barba Group (lorenabarba.com)
Huge Thanks to Marcial Sanchis, Francesco Mario D’Afiero, Gerardo Zampino, Abhijeet Vishwasrao, and Ricardo Vinuesa for their feedback on this material.

## Slide 208: umair-kth/ModelAir_CFD (github.com)